## Slide 1: Propagation of pulses in dispersive media
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 2: why do we use the propagation of pulses in dispersive media?
In telecommunications, for example, understanding dispersion is essential for optimising the fibre-optic networks that form the backbone of our Internet communications.
Even if the non-linear effects in conventional fibers are very weak, they are still present, since pulses propagate over large distances and cannot be neglected.

## Slide 3: why do we use the propagation of pulses in dispersive media?
In addition, advanced medical techniques, such as magnetic resonance imaging (MRI) and some forms of ultrasound imaging, also depend on our understanding of pulse dispersion to produce clear and accurate images.
The ability to predict and manipulate how pulses propagate through different tissues may be key to effectively diagnosing and treating various diseases.

## Slide 4: why do we use the propagation of pulses in dispersive media?
Dispersion in this context is essentially the dependence of the refractive index of the material on the frequency of the light.
This phenomenon affects how and to what depth different wavelengths of light are absorbed in the semiconductor material.
In a solar cell, optimising dispersion means maximising the absorption of light at different wavelengths to increase photovoltaic conversion efficiency.
renewable energy & solar cells

## Slide 5: why do we use the propagation of pulses in dispersive media?
Allows us to describe the propagation of an electric field along z in 3D and 1D in a Rubidium cell

## Slide 6: Description of the impulse upon entering the medium
Consider a Gaussian pulse propagating along the z-axis. At z=0, on a dispersive medium:
with a Gaussian envelope given by :
Envelope
Analytical signal

## Slide 7: Description of the impulse upon entering the medium
The positive frequency part of the signal, also known as the "analytical signal" is:
The Fourier transform of this analytical signal, which is also the positive frequency part of the electric field, is given by :
With:
FT
The shorter the pulse, the wider the spectrum!
Notes: Spectral width

## Slide 8: Description of the impulse upon entering the medium
The impulse upon entering the dispersive medium can be seen as a sum of monochromatic waves:
Propagation over a length z, each spectral component acquires a phase k(ω)z:

## Slide 9: Dispersion of the medium
By performing a second-order Taylor expansion around the center frequency ⍵p of the pulse spectrum, we obtain:
From the dispersion relation in a dielectric medium, we get:

## Slide 10: Dispersion of the medium
The third term is called the second-order dispersion or group velocity dispersion:
The second term of this development allows us to deduce the group velocity:

## Slide 11: Propagation of a Gaussian pulse
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016
: wave packet spread
: chirp
Envelope propagation at vg

## Slide 12: Phase velocity and group velocity
Describes the speed at which the envelope of a pulse propagates through a given medium.
Pulse Propagation in Dispersive Media, Rutgers university
Describes the speed at which the phase plan propagates through a given medium.

## Slide 13: Group velocity dispersion (GVD)
Responsible for pulse spreading and the appearance of a frequency chirp (variation of the instantaneous frequency along time)
The pulse widens because the different spectral components do not have the same group velocity.
Frequency-dependent
Govind P. Agrawal, Ultrashort Pulse Propagation in Nonlinear Dispersive Fibers, 2022
Front
Back
Time

## Slide 14: Group velocity dispersion (GVD)
In media with positive dispersion, the pulse acquires a positive chirp when propagating in an optical medium.
High frequencies propagate less quickly than low frequencies
Blue frequency acquires propagation delay compared to red frequency
Front
Back
Back
Front
Electric field
Electric field
Time
Time
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 15: Group velocity dispersion (GVD)
The shorter (and therefore spectrally wider) the pulse, the greater the delay.
An impulse spreads faster when it is shorter at the start, when all its spectral components were superimposed in time
z (mm)
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 16
Normale dispersion
Positive dispersion
Slow light
vg< c
Normale dispersion : slow light
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 17
Normale dispersion : slow light
The pulse envelope propagates more slowly than the speed of light in a vacuum.
The experiment, based on controlled atomic resonances, exacerbated positive dispersion to the point of reducing the group velocity of light to almost zero.
vg< c
Lene Vestergaard Hau and al., Light speed reduction to 17 metres per second in an ultracold atomic gas, 1999

## Slide 18
Anomalous dispersion
Negative dispersion
Fast light
vg<0 or vg>c
Anomalous dispersion : fast light
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 19
We can also find situations where the medium is sufficiently dispersed for vg to exceed c or even become negative.
In this case, the pulse envelope propagates backwards in the medium, and a pulse leaves the medium with a negative group delay.
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007

## Slide 20
A pulse can be thought of as the result of constructive and destructive interference between its various Fourier (frequency) components.
At the peak of the pulse, these components add up in phase, whereas they interfere destructively in the temporal edge of the pulse
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007

## Slide 21
In a material with a frequency-dependent refractive index, each frequency propagates with a different phase velocity, thereby modifying the nature of the interference.
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007

## Slide 22
The effect is to shift the peak of the pulse in time, but with the pulse shape staying the same
Just a move of the point of constructive interference occurs, both arise from the same effect: the shifting of the point of constructive interference to another point in space-time.
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007

## Slide 23
Observers at space-time points in the blue cone can see the event and those outside the cone cannot
The flow of information within the light cone is said to be relativistically causal.
Hypothetical faster-than-light propagation of information is relativistically acausal, meaning that there is no direct time-ordered link between a cause and an effect
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007

## Slide 24
All the information encoded on the waveform is available to be detected at the pulse front (although it might be difficult to measure in practice).
Thus, the fact that the peak of the pulse is advanced in time is not a violation of the special theory of relativity — so long as it never advances beyond the pulse front.
vg<0 or vg>c
Anomalous dispersion : fast light
Daniel J. Gauthier and Robert W. Boyd, Fast Light, Slow Light and Optical Precursors: What Does It All Mean?, 2007
Notes: The peak is advanced as it passes through the medium, but the pulse front is unaffected.

## Slide 25
No problem with Einsteinian causality, just because light travels at vg>c doesn't mean that information travels faster than the speed of light.
vg>c
Fast light : what about causality?

## Slide 26: Frequency drift: chirped initial pulse
We now consider the propagation in a dispersive medium of a pulse which initially presents a chirp:
FT
With C the chirp rate

## Slide 27: Frequency drift: chirped initial pulse
No initial chip :
With initial chip :
Impulse limited by fourier transform
Impulse is not limited by a Fourier transform

## Slide 28: Frequency drift: chirped initial pulse
After propagation through the dispersive medium of thickness z, the field becomes:
We can therefore write down the impulse in the following form:
And we can finally extract the pulse duration:

## Slide 29: Frequency drift: chirped initial pulse
Front
Back
Back
Front
Electric field
Electric field
Time
Time
Compresses the pulse
Fabien Bretenaker, Antoine Browaeys, Ondes électromagnétiques, 2016

## Slide 30: Frequency drift: chirped initial pulse
Amplification without damaging optical components
Pulse lasers are used in precision surgical procedures (ophthalmology for cataract surgery and vision correction)
Donna Strickland & Gérard Mourou
Satomi Shiraishi, Investigation of Staged Laser-Plasma Acceleration, 2014 Phd Thesis

## Slide 31: Phase self-modulation: Nonlinear effect
Linear effect → spectral content of the pulse remains unchanged along the propagation, dispersion is responsible for spreading the pulse:
Nonlinear effect→Phase self-modulation (PSM), result to a change in the frequency spectrum, no change in the temporal form
Kuriakose, V. C., & Porsezian, K. Elements of optical solitons: An overview. Resonance, (2010)

## Slide 32: Phase self-modulation: Nonlinear effect
The phase of the pulse depends on the intensity of the beam
The optical pulse travels over a distance L through an optical fiber, its shift in the phase is given by:
Kuriakose, V. C., & Porsezian, K. Elements of optical solitons: An overview. Resonance, (2010)
Linear frequency chirp with the GVD
Variation of instantaneous frequency by phase auto-modulation, Nonlinear frequency chirp

## Slide 33: Phase self-modulation: Nonlinear effect
We observe the propagation of a pulse, described as a scalar field, in an isotropic medium, its field is written as:
Where A(z,t) is the envelope of the pulse and ⍵p its central frequency, the intensity of this pulse, will introduce, through the Kerr effect assumed to be instantaneous, a modification of the index:

## Slide 34: Phase self-modulation: Nonlinear effect
So the additional nonlinear phase, accumulated by this wave after a length L, will be written as:
Since this phase varies with time, it leads to a variation in the instantaneous frequency of the beam:

## Slide 35: Phase self-modulation: Nonlinear effect
By injecting the field into the propagation equation and making the slowly varying envelope approximation, we obtain:
And like in the linear case,by performing a second-order Taylor expansion around the center frequency ⍵p of the pulse spectrum, we obtain:
With:
Where:

## Slide 36: Phase self-modulation: Nonlinear effect
From the two previous equations and by observing the pulse in a reference frame moving at the group velocity, and by introducing a delayed time:
we can therefore rewrite the expression:
Where:

## Slide 37: Phase self-modulation: Nonlinear effect
Ultimately, we find the same nonlinear Schrödinger equation as in the case of a continuous beam undergoing self-focusing and diffraction, with the following correspondence:
we finally obtain:
Spatial soliton
Temporal soliton
Diffraction
Dispersion
Self-focalisation
Self-modulation
x
τ
Impulsion
Beam

## Slide 38: Phase self-modulation: Nonlinear effect
In the same way as in the transverse dimension, the equation admits solutions that propagate without temporal deformation, that is, a temporal soliton:
With:
Kuriakose, V. C., & Porsezian, K. Elements of optical solitons: An overview. Resonance, (2010)
Creation of a soliton that propagates without deformation

## Slide 39: Phase self-modulation: Nonlinear effect
For the dispersion and self-phase modulation to compensate each other, D0 and n2 must have opposite signs.
Kuriakose, V. C., & Porsezian, K. Elements of optical solitons: An overview. Resonance, (2010)
One way to obtain temporal solitons is to have materials where n2 < 0 and D0 > 0

## Slide 40: Conclusion
The propagation of pulses is strongly influenced by the dispersion of the medium
Linear effect →Group velocity dispersion
High frequencies propagate less quickly than low frequencies
Responsible for pulse spreading and the appearance of a frequency linear chirp
possibility to use chirped initial pulse to compress the pulse

## Slide 41: Conclusion
The propagation of pulses is strongly influenced by the dispersion of the medium
Nonlinear effect →Self-phase modulation
No change in the temporal form
Result to a change in the frequency spectrum with the appearance of frequency nonlinear chirp

## Slide 42: Conclusion
The propagation of pulses is strongly influenced by the dispersion of the medium
Linear effect →Group velocity dispersion +
Nonlinear effect →Self-phase modulation
Compensation for both effects
Creation of a soliton that propagates without deformation

## Slide 43: Conclusion
The propagation of pulses is strongly influenced by the dispersion of the medium
In telecommunications, understanding dispersion is essential
advanced medical techniques, such as magnetic resonance imaging (MRI) and some forms of ultrasound imaging
renewable energy & solar cells
Describe the propagation of an electric field along z in 3D and 1D in a Rb cell